## Slide 1
“Digital Logic Design”
Lecture # 12

## Slide 2
SOP and POS

## Slide 3: Sum of Product
The sum-of-products (SOP) form is a method (or form) of simplifying the Boolean expressions of logic gates.
Sum and product derived from the symbolic representations of the OR and AND functions.
OR (+) , AND ( . ) , addition and multiplication.
f(A,B,C) = ABC + A’BC’
Sum
Product terms

## Slide 4: Product of Sum
When two or more sum terms are multiplied by a Boolean OR operation.
Sum terms are defined by using OR operation and the product term is defined by using AND operation.
f(A,B,C) = (A’+B) .(B+C’)
Product
Sum terms

## Slide 5: Standard SOP and POS Forms
The canonical forms are the special cases of SOP and POS forms.
These are also known as standard SOP and POS forms.

## Slide 6: Canonical Form
In SOP or POS form, all individual terms do not involve all literals.
For example AB + A’BC the first product term do not contain literal C.
If each term in SOP or POS contain all literals then the expression is known as standard or canonical form.

## Slide 7: Canonical Form
Each individual term in the POS form is called Maxterm.
Each individual term in the SOP form is called Minterm.
In Minterm, we look for the functions where the output results is “1”.
while in Maxterm we look for function where the output results is “0”.
We perform Sum of minterm also known as Sum of products (SOP) .
We perform Product of Maxterm also known as Product of sum (POS).

## Slide 8: Maxterms:
1. f(A,B,C) = (A+B+C).(A+B’+C).(A+B’+C’)+(A’+B’+C’)
= M0 + M2 + M3 + M7
= ΠM(0,2,3,7)
2. f(A,B,C)= (A+B+C’).(A+B’+C’).(A’+B+C’).(A’+B’+C’)
= M1 + M3 + M5 + M7
= ΠM (1,3,5,7)
3. f(A,B,C)= (A+B+C).(A+B’+C).(A+B’+C’).(A’+B’+C)
= M0 + M2 + M3 + M6
= ΠM (0,2,3,6)

## Slide 9
A | B | C | Minterms | Maxterms
0 | 0 | 0 | A’B’C’ = m0 | A+B+C = M0
0 | 0 | 1 | A’B’C = m1 | A+B+C’ = M1
0 | 1 | 0 | A’BC’ = m2 | A+B’+C = M2
0 | 1 | 1 | A’BC = m3 | A+B’+C’ = M3
1 | 0 | 0 | AB’C’ = m4 | A’+B+C = M4
1 | 0 | 1 | AB’C = m5 | A’+B+C’ = M5
1 | 1 | 0 | ABC’ = m6 | A’+B’+C = M6
1 | 1 | 1 | ABC = m7 | A’+B’+C’ = M7

## Slide 10
Minterms:
f(A,B,C) = A’B’C’ + A’BC’ + A’BC + ABC
= m0 + m2 + m3 + m7
= Σm(0,2,3,7)
f(A,B,C)= A’B’C + A’BC + AB’C + ABC
= m1 + m3 + m5 + m7
= Σm(1,3,5,7)
f(A,B,C)= A’B’C’ + A’BC’ + A’BC + ABC’
= m0 + m2 + m3 + m6
= Σm(0,2,3,6)